## Slide 1
Power
Distribution
LED 7 Segment Display &
Keypad
CPU, Clock & Buffers
ROM, RAM, Address Decoder
IDE Hard disk & Controller
VGA Video Controller
80 x 30 16 Colour
640 x 480 2 Colour
320 x 200 256 Colour
MCGA mode compatible
Serial & PIA
PS2 Keyboard
Sound & Joystick

## Slide 2: BREADBOARD PC 8088 INTRODUCTION PC#1

## Slide 3: WHY Use breadboards?
Breadboarding Labs Channel
  Started August 2022
  Build reliable digital electronics projects
  Using good quality breadboards
  At frequencies of 25MHz and beyond

## Slide 4: WHY Use breadboards?
Electronics engineers advise against use of Breadboards
I am an electronics hobbyist, inspired by Ben Eater on YouTube
Allows a design to evolve step by step as understanding grows
Printed Circuit Boards (PCBs) take longer and don’t allow the same flexibility or project evolution
Breadboards allow projects to be re-used and recycled

## Slide 5: BREADBOARD DISADVANTAGES
Projects can be unreliable with poor quality breadboards
Need DIP Chips or adapters for non DIP chip layouts (PLCC, LGA, TQFP)
Power distribution problems
Computer Buses cumbersome using 2 wide power strips for bus rails
Hand cut wiring can be time consuming but gives neater layouts
Use BusBoard Prototype Systems (or similar)
Retro 1980’s projects not an issue
Follow Breadboarding Tips for power distribution and volt metering
Use Stripboard bus with 0.1” connectors and Dupont ribbon cables
Dupont ribbon cables with 8 pin shells

## Slide 6: IBM PERSONAL COMPUTER (PC)
The IBM Personal Computer (PC) was released in October1981
Used the Intel 8088 version of the 8086 processor
8 bit data bus vs 16 bit for 8086
A number of 8086/8088 breadboard projects out there
  Building and programming a 16bit Intel x86 Breadboard Computer
I am not aware of any PC compatible 8088 Breadboard project (PCB Only)

## Slide 7: Breadboard PC - Intel 8088 PC-XT Hybrid
OS
Run an early version of MS-DOS (3.3x) or PC-DOS (2.11)
Video
Monochrome Display Adaptor (MDA) compatible
1981 PC and PC-XT
Clock, CPU and bus control, 8-bit ISA Bus
Direct Memory Access (DMA) controller and Timer
8255 Port and Speaker
PC-AT
Real time clock
Dual Interrupt Controllers (IRQ0-15, PC/XT IRQ0-7) Mouse/Network Card
IBM PS/2
PS/2 Keyboard, Mouse and 8042 Controller,
3.5” 1.44MB Floppy Disk Drive & controller
MCGA Display Adaptor (CGA + 640x480 2 colour, 320x200 256 colour)
Compaq Deskpro 386
IDE Disk and Controller
80 x 25 with 8x16 Character ROM for VGA output

## Slide 8: WHY BOTHER WITH A BREADBOARD PC?
Nanocomp 6809 Project now complete
  Project started in 1981on PCBs and wiring pen
  Re-started in 2020 now on 18 breadboards (& 18 power bus rails)
  VGA compatible video and graphics runs Tetris, Lunar Lander and displays 256 Colour PNG Images
  Learnt a massive amount, especially about computer video generation
I’ve been using PCs since 1987 but not much ‘under the hood’
  Aim to understand all hardware, BIOS and MS-DOS internals
No one else appears to have done it
Experts advise against large/complex breadboard projects – but wire wrap OK

## Slide 9
Original IBM PC Prototype Wire wrap board

## Slide 10: LESSONS LEARNED FROM 6809 NANOCOMP SERIES
Videos were organised by project steps
Most videos too long – 30-60 minutes even when split into multiple parts
Large gaps of many weeks between publishing new videos
Video post-production takes longer (Editing, Subtitles and Reviewing)
Plan to keep videos to 15-20 minutes maximum
Publish more frequently - not based on completed project steps
All videos have reviewed/edited English sub-titles
Recommend view at 1.5+ times speed with sub-titles

## Slide 11: High LEVEL PLAN
Clock and Reset
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 13: BREADBOARD PC 8088 #2 HIGH LEVEL DESIGN

## Slide 14: High LEVEL PLAN
Clock and Reset
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 15: BACKGROUND INFO
Personal Computer World November 1981
The 8088 Project Book Robert Grossblatt 1989
PC-XT Technical Reference
PC-AT Technical Reference
PS/2 Technical Reference
Compaq Deskpro 386 Technical Reference 1986 and 1988 versions
Sergey Kiselev XI_8088 https://github.com/skiselev/xi_8088/tree/main
Wireless World July 1981 Nanocomp 6809 (LED Display and keypad)
KiCad schematic
Nanocomp Monitor in C

## Slide 16: The 8088 Project Book Robert Grossblatt
My favourite “Laws of Life and Design” https://archive.org/details/the_8088_project_book_grossblatt_robert_1989
  Golden rule “Think for yourself”
  Dynamic RAM - “Using dynamic RAM in a single board system like ours is, in words of two syllables, a mistake.”
  1 Know what you want to do before you try to do it
  4 There's no substitute for a data sheet
  8 If you can't afford to blow it up you can't afford to use it
  11 If you only see one solution, you don't understand the problem
  17 Machine language gives you total control of everything
  21 It's more important to get it working than get it perfect
  28 Anything which can blow up will blow up
  57 Important things only happen when you’re not watching them
  80 A circuit of a thousand parts starts with an LED
  93 Software, unlike life, lets you change horses in midstream

## Slide 17: USE EARLY 1980s components WHERE POSSIBLE
The following exceptions for practicality, cost and/or availability
  Static RAM over legacy Dynamic RAM – reduces chip count for buffers, no refresh, no wait states (Grossblatt “a mistake”)
  Modern EEPROM over legacy EPROM – simplifies programming, no wait states or UV
  Programmable logic devices (PLD) to simplify logic and decoding (used in mid 80’s designs)
  3.5” Floppy Disk and PS/2 Keyboard & Mouse (introduced 1987)
  2.5” SATA Hard Disk with SATA-IDE converter (Avoid legacy IDE disks & 12V PSU)
  Video - VGA LCD Monitor at 640 x 400@70Hz vs Monochrome 720 x 350@50Hz

## Slide 18: WHY MONOCHROME DISPLAY ADAPTOR (MDA)
Why not CGA/EGA/VGA?
Need PC compatibility for standard PC software to work
Nanocomp Video Controller produced VGA output but was not PC register compatible
MDA simpler to develop using dual port RAM
EGA and VGA used custom VLSI chips for control registers etc – 160 pin for breadboards!
MDA and other video cards can co-exist for debugging

## Slide 19: MONOCHROME DISPLAY ADAPTOR (MDA)
Plan to develop CGA (or MCGA) in later stages of project
MDA has hard coded ROM based fonts and 4K Video RAM
No Parallel Port required
Use VGA Video DAC Palette chip as simpler to produce video output for VGA
  MDA Adaptor could do 16 colours with some versions and colour monitor!
80 Columns by 25 rows, 1 byte character, 1 byte attributes/colour 4000 bytes
MDA 720 x 350 with 9 x 14 Characters at 50 Hz (18.4KHz Horizontal Sync)
Drop 9 pixel wide characters, make them 8 x 16 like VGA
MDA (VGA out) 640 pixels x 400 lines, 8 x 16 Characters at 70Hz (31.5KHz HS)

## Slide 20: NanOCOMP ‘8088’ Block DIAGRAM
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
Memory Map
00000-7FFFF RAM (Y1)
80000-8FFFF PIA (Y4)
FFC00-FFFFF ROM (Y7)
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder

## Slide 21: High LEVEL PLAN
Clock and Reset
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 22: BREADBOARD 8088 PC#3 RESET & SUPERVISOR

## Slide 23: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 24: NanOCOMP ‘8088’ Block DIAGRAM
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
Memory Map
00000-7FFFF RAM (Y1)
80000-8FFFF PIA (Y4)
FFC00-FFFFF ROM (Y7)
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder

## Slide 26: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 27: BREADBOARD 8088 PC#4 CLOCK

## Slide 28: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 29: NanOCOMP ‘8088’ Block DIAGRAM
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
Memory Map
00000-7FFFF RAM (Y1)
80000-8FFFF PIA (Y4)
FFC00-FFFFF ROM (Y7)
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder

## Slide 31: The 8088 Project Book Robert Grossblatt
My favourite “Laws of Life and Design” https://archive.org/details/the_8088_project_book_grossblatt_robert_1989
  Golden rule “Think for yourself”
  Dynamic RAM - “Using dynamic RAM in a single board system like ours is, in words of two syllables, a mistake.”
  1 Know what you want to do before you try to do it
  4 There's no substitute for a data sheet
  8 If you can't afford to blow it up you can't afford to use it
  11 If you only see one solution, you don't understand the problem
  17 Machine language gives you total control of everything
  21 It's more important to get it working than get it perfect
  28 Anything which can blow up will blow up
  57 Important things only happen when you’re not watching them
  80 A circuit of a thousand parts starts with an LED
  93 Software, unlike life, lets you change horses in midstream

## Slide 32
Intel 8284A
Fujitsu MBL8284A
CLK

## Slide 33: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 34: BREADBOARD 8088 PC#5 CPU NOP WITH LOGIC ANALYZER

## Slide 35: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 36: NanOCOMP ‘8088’ Block DIAGRAM
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
Memory Map
00000-7FFFF RAM (Y1)
80000-8FFFF PIA (Y4)
FFC00-FFFFF ROM (Y7)
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder

## Slide 38
IBM PC-XT Technical Reference Guide Appendix B-15 page 449

## Slide 39: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 40: BREADBOARD 8088 PC #6 BUS CONTROLLER, LATCHES & BUFFERS

## Slide 41: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 42: NanOCOMP ‘8088’ Block DIAGRAM
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
Memory Map
00000-7FFFF RAM (Y1)
80000-8FFFF PIA (Y4)
FFC00-FFFFF ROM (Y7)
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder

## Slide 44: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM & RAM
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 45: BREADBOARD 8088 PC #7 EEPROM, RAM & ADDRESs DECODER

## Slide 46: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 47: NanOCOMP ‘8088’ Block DIAGRAM
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder
Memory Map
00000-7FFFF RAM (512K)
D0000-DFFFF PIA (64K)
F8000-FFFFF ROM (32K)

## Slide 48: XI 8088 ROM AND RAM SCHEMATIC
AT28C256

## Slide 49: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC
Test Program in 8086 Assembler Testing Program in ROM
Writing to then reading from RAM

## Slide 50: BREADBOARD 8088 PC #8 8086 ASSEMBLER & TESTING EEPROM & RAM

## Slide 51: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC
Test Program in 8086 Assembler Testing Program in ROM
Writing to then reading from RAM

## Slide 52: 8086 ASSEMBLY LANGUAGE
Tool chain set up by Slador “Toolchain setup for 16-bit Intel 8088 and 80188 step by step”
  https://www.youtube.com/watch?v=708uKGdqROk
  NASM for Assembler
Xi 8088 / Sergey's XT BIOS for Reset handling https://github.com/skiselev/xi_8088
8086 Segmented Memory Model with 16-bit registers (64K) but 1 MB 20-bit address range
  CS (code segment), DS (data segment), SS (stack segment), and ES (extra segment).
  TESTRAM Program uses Data Segment Register – DS & Data Index Register – DI
  Physical Address = DS x 16 (rotate Left 4) + DI
  Reset Address FFFF0 = 1MB – 16 (10h), The CS register is set to FFFF 16, IP 0000
  CS = FFFF, IP = 0000 [FFFF:0000]
  Use DS and DI to access RAM
  Can’t ADD CMP or TEST Segment registers, have to copy to another register first
Intel iAPX 88 BOOK http://bitsavers.informatik.uni-stuttgart.de/components/intel/8086/210200-002_iAPX88_Book_1983.pdf

## Slide 53: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 54: BREADBOARD 8088 PC #9 LED DISPLAY & KEYPAD

## Slide 55: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 56
Nanocomp Schematic
Wireless World July 1981

## Slide 57: LED DISPLAY PIN MAPPING
PA3 - A
PA1 - B
PA2 - C
PA4 - D
PA5 - E
PA6 - F
PA0 - G
PIA Signals
PA0-PA6
PB0-PB3
RESET
GND
NMI

## Slide 58: ULN2803A Darlington Transistor Array
No need for 5.6K from PA0-PA6
Direct connection OK
“The ULN2803A device has a 2.7-kΩ series base resistor for each Darlington pair for operation directly with TTL or 5-V CMOS devices.”

## Slide 59: KEYPAD and DECODER
PIA Signals
PA0-PA6
PB0-PB3
RESET
GND
NMI
Keypad PA6

## Slide 60: KEYPAD and DECODER
PA0 - 5 6 F R
PA1 - 8 9 E M
PA2 - 2 3 0 I
PA3 - A B C D
PA4 - 7 4 1
PA5 - L S CN G
PA6 -
Q0 - 5 8 2 A 7 L
Q1 - 6 9 3 B 4 S (P)
Q2 - F E 0 C 1 CN
Q3 - R M I D G
RST - RESET
AB - NMI

## Slide 61: KEYPAD and DECODER
L Load | S Save | CN Continue | G Go | RST Reset
A | B | C | D | AB Abort
7 | 8 | 9 | E | M Memory
4 | 5 | 6 | F | R Register
1 | 2 | 3 | 0 | I Increment
 | PA0 | PA1 | PA2 | PA3 | PA4 | PA5 | PA6
Q0 | 5 | 8 | 2 | A | 7 | L | -
Q1 | 6 | 9 | 3 | B | 4 | S(P) | -
Q2 | F | E | 0 | C | 1 | CN | -
Q3 | R | M | I | D | - | G | -

## Slide 62
View from underside of stripboard

## Slide 63
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
View from underside of stripboard,
parts hidden

## Slide 64
View from underside of stripboard

## Slide 65
X
X
X
X
X
X
X
View from underside of stripboard,
parts hidden

## Slide 66: Testing the Nanocomp 8088 – E & F SEGMENTS
Nanocomp design expects E & F reversed compared to 7 Segment LED Data sheet
Character values affected
2 4 5 9 d
Review Schematic Diagram
PA5 -> F
PA6 -> E
PA0 - G
PA1 - B
PA2 - C
PA3 - A
PA4 - D
PA5 - E
PA6 - F
PA0 - G
PA1 - B
PA2 - C
PA3 - A
PA4 - D
PA5 - F
PA6 - E

## Slide 67: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC
Look at Fritzing plans of display & Keypad
Test Program in 8086 Assembler
Program EEPROM
Check LED display and Key codes

## Slide 68: BREADBOARD 8088 PC #10 LED DISPLAY & KEYPAD SOFTWARE & TESTING

## Slide 69: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC
Look at Fritzing plans of display & Keypad
Test Program in 8086 Assembler
Program EEPROM
Check LED display and Key codes

## Slide 70
Nanocomp Schematic
Wireless World July 1981

## Slide 71: KEYPAD and DECODER
L 0x05 | S 0x15 | CN 0x25 | G 0x35 | RST Reset
A 0x03 | B 0x13 | C 0x23 | D 0x33 | AB Abort
7 0x04 | 8 0x01 | 9 0x11 | E 0x21 | M 0x31
4 0x14 | 5 0x00 | 6 0x10 | F 0x20 | R 0x30
1 0x24 | 2 0x02 | 3 0x12 | 0 0x22 | I 0x32
 | PA0 | PA1 | PA2 | PA3 | PA4 | PA5 | PA6
Q0 | 5 | 8 | 2 | A | 7 | L | -
Q1 | 6 | 9 | 3 | B | 4 | S(P) | -
Q2 | F | E | 0 | C | 1 | CN | -
Q3 | R | M | I | D | - | G | -

## Slide 72
View from underside of stripboard

## Slide 73
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
View from underside of stripboard,
parts hidden

## Slide 74
View from underside of stripboard

## Slide 75
X
X
X
X
X
X
X
View from underside of stripboard,
parts hidden

## Slide 76: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 77: BREADBOARD 8088 PC #11 NANOCOMP MONITOR TO 8086/8088

## Slide 78: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 79: WHY DO WE NEED A MONITOR PROGRAM?
Apple I included WozMon in 248 bytes
  Ben Eater https://youtu.be/HlLCtjJzHVI?si=C_-FtWSOUDYZLrdE
Tim Paterson (Seattle Computer Products) 86-DOS Early version of DEBUG in ROM, became DEBUG.EXE in MS-DOS
BASIC ROM in PET, BBC Micro, Spectrum, Dragon 32, TRS 80 etc provided similar features (but in 4K-16K)

## Slide 80: WHY DO WE NEED A MONITOR PROGRAM?
The Nanocomp Monitor is a very simple ‘operating system’ in 1K ROM
  Initializes Stack, Reset & Interrupt Vectors (& 8088 Segment Registers)
  Inspecting and changing memory
  Executing programs
  Displaying register values after breakpoints (SWI 0x3F, INT3 0xCC).
  Loading and saving of memory over the serial port (originally was save/load to/from audio cassette) in S-Record Format (SREC)
Original Monitor in Motorola 6800 Assembly code
  Updated to work with 6809 in July 1981
#12 Reverse Engineered/disassembled with help from Mike Spivey Nanocomp 6802 ROM disassembly https://github.com/Spivoxity/nanocomp/blob/master/rom.m68
Need 8088 Monitor to build & test hardware to run & debug an XT BIOS
When BIOS is operational, running MS-DOS possible

## Slide 81: the Nanocomp MONITOR
Monitor Commands
M - Memory inspect/change
G - Go execute program at given address
S - Save to serial port in SREC
L - Load from serial port in SREC
CN - Continue from INT3
R - Register display after INT3
I - Increment, used by M and R
RS - Hard Reset, same as power cycle
AB - Abort Non Maskable Interrupt (NMI) – Display Registers
L 0x05 | S 0x15 | CN 0x25 | G 0x35 | RST Reset
A 0x03 | B 0x13 | C 0x23 | D 0x33 | AB Abort
7 0x04 | 8 0x01 | 9 0x11 | E 0x21 | M 0x31
4 0x14 | 5 0x00 | 6 0x10 | F 0x20 | R 0x30
1 0x24 | 2 0x02 | 3 0x12 | 0 0x22 | I 0x32

## Slide 82: 6809 – 8088 Conversion ISSUES
No PUSHA or POPA (only 80188+), have to do each register individually
Used JP and not JMP (Jump Parity!!, JP Is Z80 JMP)
Using CALL address (and code segment) in registers
  needs indirect call to save address & code segment in RAM
No way to change segments from Monitor, use top 64K RAM 70000-7FFFF
  CS – F000 (Monitor code in EEPROM)
  DS – 7000
  SS – 7000
  ES – D000 (PIA and Serial Port)

## Slide 83: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 84: BREADBOARD 8088 PC #12 SERIAL PORT HARDWARE & SOFTWARE

## Slide 85: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 86: NanOCOMP ‘8088’ Block DIAGRAM
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder
Memory Map
00000-7FFFF RAM (512K)
D0000-DFFFF PIA & UART
F8000-FFFFF ROM (32K)
3.6Mhz
Clock
FT232RL
Baud Rate
1,843,200 Hz
÷ 16=115,200
÷ 64=28,800
Serial Port (ACIA/UART)
PC USB
Baud Rate
3,686,400 Hz
÷ 16=230,400
÷ 64=57,600

## Slide 87: SERIAL PORT & MONITOR SAVE/LOAD
Serial Port – Motorola MC68B50 ACIA
(Asynchronous Communication Interface Adapter)
Register Select x 1 and R/W control access to port and control registers
Clock divide by 1, 16 or 64 by control register
Interrupt on Transmit Data Register Empty (TDRE) or Receive Data Register Full (RDRF)
No need for RS-232 (+/- 12v), use FTDI Compatible Serial –TTL adaptor (FT232RL)
Virtual COM port on PC using USB (CDM v2.12.36.4 WHQL Certified driver)
FT232RL MC68B50
GND GND
/CTS /RTS – Request to Send Output same as /DTR
5V Not Connected – will power Nanocomp from PC
TX RX – cross over as DTE to DTE
RX TX – cross over as DTE to DTE
/RTS (Not /DTR) /CTS – Clear to Send Input

## Slide 88: MOTOROLA S19-SREC FILE FORMAT
SREC Text format for binary assembler output
Record Type Hexadecimal Character
S1
Count 2 Char. No. of Bytes inc. Address & Checksum
Address 4 Char. 16 Bit Address in Hex
Data (Count – 3) x 2 Data Char.
Checksum Complement (Count + Address + Data values)
For No data Count=03 for Address + Checksum
S9
Count 03
Address 0000 Execution address not used
Checksum $FC (03 1’s complement NOT)
Notepad++ validates SREC and Checksum
LED Display F – Finished
C – Checksum Error
E – Hexadecimal conversion Error

## Slide 89: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 90: BREADBOARD 8088 PC #13 MONOCHROME DISPLAY ADAPTOR (MDA#1)

## Slide 91: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 92: WHY MONOCHROME DISPLAY ADAPTOR (MDA)
Why not CGA/EGA/VGA?
Need PC compatibility for standard PC software to work
Nanocomp 6809 Video Controller produced VGA output but was not PC register compatible
MDA simpler to develop using dual port RAM
EGA and VGA used custom VLSI chips for control registers etc – 144-160 pins for breadboards!
MDA and other video cards can co-exist for debugging

## Slide 93
MC6845 CRTC, Character ROM, 8 RAM + 56 TTL logic chips
66 Chips in Total

## Slide 94: MONOCHROME DISPLAY ADAPTOR (MDA)
Plan to develop CGA (or MCGA) in later stages of project
MDA has hard coded ROM based fonts and 4K Video RAM
No Parallel Port required
Use VGA Video DAC Palette chip - simpler for VGA video output for LCD Monitors
  MDA Adaptor could do 16 colours with some versions and colour monitor!
  https://www.seasip.info/VintagePC/mda.html#cmda
80 Columns by 25 rows, 1 byte character, 1 byte attributes/colour 4000 bytes
MDA 720 x 350 with 9 x 14 Characters at 50 Hz (18.4KHz Horizontal Sync)
Drop 9 pixel wide characters, make them 8 x 16 like VGA
MDA (VGA out) 640 pixels x 400 lines, 8 x 16 Characters at 70Hz (31.5KHz HS)

## Slide 96
HD68A45S
3.7Mhz Clk
Cursor Skew
Disp En. Skew
4K Dual Port RAM
IMSG176 DAC
256 Colours
262K Palette

## Slide 97: Why MOTOROLA 6845/HITACHI HD68A45S
Used by Commodore PET, BBC Micro and IBM MDA & CGA Adaptor
Flexible, not constrained like MC6847 (Dragon32, Tandy Color)
Can address 16K in characters with up to 32 rows (512KBytes total)
Designed for Character based but can be used for Graphics
Can work at 3+MHz Character clock (25.175/8 = 3.147MHz)
H Sync and V Sync may need to be inverted for some VGA Modes
Light pen not used

## Slide 98: VGA VIDEO STANDARD
Introduced by IBM in PS/2 range in 1987
Analogue Red, Green, Blue colour signals between 0V and 0.7V
TTL Levels for Vertical Sync and Horizonal Sync (+ve & -ve)
Replaced MDA, CGA and EGA monitors (digital inputs)
256 Colour Palette 18 bit/262K (CGA 16, EGA 64)
Fonts 9x16 or 8x16 (8 wide, 16 high), 9x14 MDA, 8x8 CGA
15 Pin Sub Miniature ‘D’ Connector, Female for computer
Video Timing data http://tinyvga.com/vga-timing
  VGA 640x480@60 Hz Industry standard (pixel clock 25.175 MHz) (30x80 characters)
  VGA 640x400@70 Hz (pixel clock 25.175 MHz) (25x80 characters)

## Slide 99: MOTOROLA 6845/HITACHI HD68A45S
2 Addresses configurable by 19 Registers (RS=0 Address, RS=1 Data)
VS – Vertical Sync, once per frame/page 70 Hz Refresh Rate
HS – Horizontal Sync, once per pixel row, 31.468KHz/31.77uS
Explanation of CRT and Sync
  https://digilent.com/reference/learn/programmable-logic/tutorials/vga-display-congroller/start
6845 CRTC Register Timing https://mrboot.de/mc6845.php
Memory Address MA0-MA13 Selects character address in RAM
Row Address RA0-RA4 Selects character raster row from ROM
Cursor and Display enable signals need to be delayed by 1+ Char Clock
HD68A45S has Skew settings for Cursor & Display enable, 1-2 Char Clocks
CRTC MA0 to Video RAM VA1
Character Clock/2 as VA0 to switch RAM from Character to Attributes

## Slide 100: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 101: BREADBOARD 8088 PC #14 MONOCHROME DISPLAY ADAPTOR (MDA#2)

## Slide 102: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 103
HD68A45S
3.7Mhz Clk
Cursor Skew
Disp En. Skew
4K Dual Port RAM
IMSG176 DAC
256 Colours
262K Palette
2 x PLD
Video Out
Attribute Mux

## Slide 104
MDA #1
ISA Bus & Buffers

## Slide 105
MDA #2
CRTC, Video RAM and Address Multiplexers
4K Dual Port RAM
CRTC Driven by
inverted Character Clock

## Slide 106
MDA #3
Clocks, timing and delay logic
Jumper only used for IBM Testing - Ignore
HRES must be 1
–HRES=0
A=0, B=0
Divide by 9 CharacterClock & Q5 S/L Latch
U43 is a 74S32 Quad OR gate, this works out to be a NOR which is wrong!
-CLR Video goes low when both delayed DE 1Q and 3Q outputs are low, goes high on 1Q low to high. Used to clear some Flip flops and latches. May need to delay HS and VS by 1 CCLK.
U100 OR gate!
NOR with U6

## Slide 107
MDA #4
Address Decoding, CRT Status Port (3BA)
-SEL 1 CRT Control (3B8)
-STATUS SEL 1 CRT Status (3BA)
/Y6 A19,A17,A16=1 A15=0 B0000-B7FFF
3B0-3BF
CRT Status Port (3BA)
True MDA 1&2=0, 4-7=1

## Slide 108
MDA #5
Attribute and video control
+S DOTS Output from Shift Reg. & Character Generator
Underline F1 & row 12
Fore Att at2,at1,at0
Back Att at6,at5,at4
F0,B0 Non-display,
B7 Reverse
At7 Blink
At3 Intensity Foreground
At7 Intensity Background,
Blink Disable
At7 Blink, Blink Enable, +Blink Chr,
-Cursor
Cursor Blink freq. = Vert Sync / 16
Character Blink freq. = Vert Sync / 32
A
B
C
D
E
F
G
AlphaDots controls Mux for F&B Intensity, RVV does not reverse F/B Intensity!
B&W Video controls output video & includes RVV
-CLR Video goes low with delayed DE but goes high 1 CClk BEFORE delayed DE
H
Colour MDA

## Slide 109
MDA #5 Old version
Attribute and video control
+S DOTS Output from Shift Reg. & Character Generator
Underline F1 & row 12
Fore Att at2,at1,at0
Back Att at6,at5,at4
F0,B0 Non-display,
B7 Reverse
At7 Blink
At3 Intensity Foreground
At7 Intensity Background,
Blink Disable
At7 Blink, Blink Enable, +Blink Chr,
-Cursor
Cursor Blink freq. = Vert Sync / 16
Character Blink freq. = Vert Sync / 32
A
B
C
D
E
F
G
Colour MDA

## Slide 110
MDA #6
Data Bus Buffers & Latches

## Slide 111
MDA #7
Video Output & CRT Control Port (3B8)
Extend C0h-DFh by 1 bit for 9 wide
CC7,CC6=1, CC5=0 C0-DF
B/W
CRT Control Port (3B8)
Colour MDA
Colour MDA
Colour MDA
Red, Green, Blue

## Slide 112
MDA #10
Character Generator, Shift Register
Note JUMPER only used for IBM testing
But could select higher ROM 8x8 characters via A12
A12 = 0 for now
Right hand character bit to widen
Graphic characters C0h-DFh to 9 bits
Character bits for
Graphic characters C0h-DFh to 9 bits
SERIN provides 9th pixel
Character Generator A0-A3=RA0-RA3
A4-A11=CC0-CC7, A12=0
-CLR Video goes low with delayed DE but goes high 1 ChClk BEFORE delayed DE

## Slide 113: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
25.175Mhz
Shift Register
74ALS166
Main Address Bus
Character Generator ROM
Main Data Bus
Row 0-15 (A0-A3)
Character
Clock 3.146Mhz
Dot Clock
Shift Reg. Latch
Video RAM
Dual Port (4Kb)
Vid. Add.
Character 0-255
(A4-A11)
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable, Cursor
Fore/Back
Clock PLD
ATF22V10
D Type Latch
7ALS574
D Type Latch
7ALS574
Attributes/RGBI
DAC
IMS G176
Attribute
Multiplexer
ATF16V8
VGA
/Display Enable
Character raster
bits
MA0
Dot Clk/4
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
Video Out PLD
ATF22V10
Blink Clock
Cursor

## Slide 114: BREADBOARD 8088 PC #15 MONOCHROME DISPLAY ADAPTOR (MDA#3)

## Slide 115: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 116: NanOCOMP ‘8088’ Block DIAGRAM – I/O PORT CHANGES
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder
Memory Map
00000-7FFFF RAM (512K)
IO D000,D100 PIA & UART
B0000-B7FFF MDA RAM (4K)
F8000-FFFFF ROM (32K)
3.6Mhz
Clock
FT232RL
Baud Rate
1,843,200 Hz
÷ 16=115,200
÷ 64=28,800
Serial Port (ACIA/UART)
PC USB
Baud Rate
3,686,400 Hz
÷ 16=230,400
÷ 64=57,600

## Slide 117: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
25.175Mhz
Shift Register
74ALS166
Main Address Bus
Character Generator ROM
Main Data Bus
Row 0-15 (A0-A3)
Character
Clock 3.146Mhz
Dot Clock
Shift Reg. Latch
Video RAM
Dual Port (4Kb)
Vid. Add.
Character 0-255
(A4-A11)
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable, Cursor
Fore/Back
Clock PLD
ATF22V10
D Type Latch
7ALS574
D Type Latch
7ALS574
Attributes/RGBI
DAC
IMS G176
Attribute
Multiplexer
ATF16V8
VGA
/Display Enable
Character raster
bits
MA0
Dot Clk/4
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
Video Out PLD
ATF22V10
Blink Clock
Cursor
IO Port Decoder

## Slide 118: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 119: BREADBOARD 8088 PC #16 MONOCHROME DISPLAY ADAPTOR (MDA#4)

## Slide 120: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Timer & Speaker
POST Port
DMA Controller
Interrupt Controller
Real time clock
Floppy Disk Controller
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 121: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD Test clock and IO decoder
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 122: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
25.175Mhz
Main Address Bus
Main Data Bus
Character
Clock 3.146Mhz
Dot Clock
Video RAM
Dual Port (4Kb)
Vid. Add.
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable
Clock PLD
ATF22V10
DAC
IMS G176
VGA
/Display Enable
MA0
Dot Clk/4
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
IO Port Decoder

## Slide 123: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD Test clock and IO decoder
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 124: BREADBOARD 8088 PC #17 MONOCHROME DISPLAY ADAPTOR (MDA#5)

## Slide 125: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD Test clock and IO decoder
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 126: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
25.175Mhz
Main Address Bus
Main Data Bus
Character
Clock 3.146Mhz
Dot Clock
Video RAM
Dual Port (4Kb)
Vid. Add.
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable
Clock PLD
ATF22V10
DAC
IMS G176
VGA
/Display Enable
MA0
Dot Clk/4
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
IO Port Decoder

## Slide 127: BIOS & CGA COLOURS (ALSO MDA) – PC-XT Tech Reference
Brown CGA
IBM CGA Monitor changed Dark Yellow to Brown by reducing Green in hardware
White – Gray
Gray – Dark Gray

## Slide 128: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 129: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 130
https://www.aceinnova.com/en/electronics/cga-and-the-brown-color-in-ibm-5153-color-display/

## Slide 131: BREADBOARD 8088 PC #18 MONOCHROME DISPLAY ADAPTOR (MDA#6)

## Slide 132: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 136: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 137: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
25.175Mhz
Shift Register
74ALS166
Main Address Bus
Character Generator ROM
Main Data Bus
Row 0-15 (A0-A3)
Character
Clock 3.146Mhz
Dot Clock
Shift Reg. Latch
Video RAM
Dual Port (4Kb)
Vid. Add.
Character 0-255
(A4-A11)
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable, Cursor
Fore/Back
Clock PLD
ATF22V10
D Type Latch
7ALS574
D Type Latch
7ALS574
Attributes/RGBI
DAC
IMS G176
Attribute
Multiplexer
ATF16V8
VGA
/Display Enable
Character raster
bits
MA0
Dot Clk/4
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
Video Out PLD
ATF22V10
Blink Clock
Cursor
IO Port Decoder

## Slide 138: VGA AND MDA FONTS
Fontraption and VGAfonts-20-11-25-with-previews.zip
https://int10h.org/blog/2019/05/fontraption-vga-text-mode-font-editor/
VGA 8 bits wide x 16 high
MDA 9 bits wide x 14 high
MDA Underline RA=12 (0xC)
VGA Underline RA=14 (0xE)

## Slide 139: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 140: BREADBOARD 8088 PC #19 MONOCHROME DISPLAY ADAPTOR (MDA#7)

## Slide 141: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 142: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
Blink PLD
25.175Mhz
Shift Register
74ALS166
Main Address Bus
Character Generator ROM
Main Data Bus
Row 0-15 (A0-A3)
Character
Clock 3.146Mhz
Dot Clock
Shift Reg. Latch
Video RAM
Dual Port (4Kb)
Vid. Add.
Character 0-255
(A4-A11)
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable, Cursor
Fore/Back
Clock PLD
ATF22V10
D Type Latch
7ALS574
D Type Latch
7ALS574
Attributes/RGBI
DAC
IMS G176
Attribute
Multiplexer
ATF16V8
VGA
/Display Enable
Character raster
bits
MA0
Dot Clk/4
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
Video Out PLD
ATF22V10
Blink Clocks
Cursor
IO Port Decoder
CRT Control
CRT Status

## Slide 143
HD68A45S
3.7Mhz Clk
Cursor Skew
Disp En. Skew
4K Dual Port RAM
IMSG176 DAC
256 Colours
262K Palette
3 x PLD
Video Out
Attribute Mux
Blink Clock

## Slide 144
MDA #1
ISA Bus & Buffers

## Slide 145
MDA #2
CRTC, Video RAM and Address Multiplexers
4K Dual Port RAM
CRTC Driven by
inverted Character Clock

## Slide 146
MDA #3
Clocks, timing and delay logic
Jumper only used for IBM Testing - Ignore
HRES must be 1
–HRES=0
A=0, B=0
Divide by 9 CharacterClock & Q5 S/L Latch
U43 is a 74S32 Quad OR gate, this works out to be a NOR which is wrong!
-CLR Video goes low when both delayed DE 1Q and 3Q outputs are low, goes high on 1Q low to high. Used to clear some Flip flops and latches. May need to delay HS and VS by 1 CCLK.
U100 OR gate!
NOR with U6

## Slide 147
MDA #4
Address Decoding, CRT Status Port (3BA)
-SEL 1 CRT Control (3B8)
-STATUS SEL 1 CRT Status (3BA)
/Y6 A19,A17,A16=1 A15=0 B0000-B7FFF
3B0-3BF
CRT Status Port (3BA)
CRT Status Port (3BA)
True MDA 1&2=0, 4-7=1

## Slide 148
MDA #5
Attribute and video control
+S DOTS Output from Shift Reg. & Character Generator
Underline F1 & row 12
Fore Att at2,at1,at0
Back Att at6,at5,at4
F0,B0 Non-display,
B7 Reverse
At7 Blink
At3 Intensity Foreground
At7 Intensity Background,
Blink Disable
At7 Blink, Blink Enable, +Blink Chr,
-Cursor
Cursor Blink freq. = Vert Sync / 16
Character Blink freq. = Vert Sync / 32
A
B
C
D
E
F
G
AlphaDots controls Mux for F&B Intensity, RVV does not reverse F/B Intensity!
B&W Video controls output video & includes RVV
-CLR Video goes low with delayed DE but goes high 1 CClk BEFORE delayed DE
H
Colour MDA
Video Enable=0
Att0-7=0
Non-display

## Slide 149
MDA #6
Data Bus Buffers & Latches

## Slide 150
MDA #7
Video Output & CRT Control Port (3B8)
Extend C0h-DFh by 1 bit for 9 wide
CC7,CC6=1, CC5=0 C0-DF
B/W
CRT Control Port (3B8)
Colour MDA
Colour MDA
Colour MDA
Red, Green, Blue
H Sync only enabled after reset when +Video Enable set for 1st time

## Slide 151
MDA #10
Character Generator, Shift Register
Note JUMPER only used for IBM testing
But could select higher ROM 8x8 characters via A12
A12 = 0 for now
Right hand character bit to widen
Graphic characters C0h-DFh to 9 bits
Character bits for
Graphic characters C0h-DFh to 9 bits
SERIN provides 9th pixel
Character Generator A0-A3=RA0-RA3
A4-A11=CC0-CC7, A12=0
-CLR Video goes low with delayed DE but goes high 1 ChClk BEFORE delayed DE

## Slide 152: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 153: BREADBOARD 8088 PC #20 MONOCHROME DISPLAY ADAPTOR (MDA#8)

## Slide 154: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 155: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
Blink PLD
25.175Mhz
Shift Register
74ALS166
Main Address Bus
Character Generator ROM
Main Data Bus
Row 0-15 (A0-A3)
Character
Clock 3.146Mhz
Dot Clock
Shift Reg. Latch
Video RAM
Dual Port (4Kb)
Vid. Add.
Character 0-255
(A4-A11)
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable, Cursor
Clock PLD
ATF22V10
D Type Latch
7ALS574
D Type Latch
7ALS574
Attributes/RGBI
DAC
IMS G176
Attribute
Multiplexer
ATF16V8
VGA
Display Enable
Character raster
bits
MA0
Dot Clk/8
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
Video Out PLD
ATF22V10
Blink Clocks
Cursor
IO Port Decoder
CRT Control
CRT Status
Fore/Back
Video En, Blink En, B/W
Video En, Blink En, B/W

## Slide 156
MDA #5
Attribute and video control
+S DOTS Output from Shift Reg. & Character Generator
Underline F001 & row 12
Fore Att at2,at1,at0
Back Att at6,at5,at4
F0,B0 Non-display
F0,B111 Reverse Video
At7 Blink
At3 Intensity Foreground
At7 Intensity Background,
Blink Disable
At7 Blink, Blink Enable, +Blink Chr,
-Cursor
Cursor Blink freq. = Vert Sync / 16
Character Blink freq. = Vert Sync / 32
A
B
C
D
E
F
G
AlphaDots controls Mux for F&B Intensity, RVV does not reverse F/B Intensity!
B&W Video controls output video & includes RVV
-CLR Video goes low with delayed DE but goes high 1 CClk BEFORE delayed DE
H
Colour MDA
Video Enable=0
Att0-7=0
Non-display

## Slide 157
MDA #7
Video Output & CRT Control Port (3B8)
Extend C0h-DFh by 1 bit for 9 wide
CC7,CC6=1, CC5=0 C0-DF
B/W
CRT Control Port (3B8)
Colour MDA
Colour MDA
Colour MDA
Red, Green, Blue
H Sync only enabled after reset when +Video Enable set for 1st time

## Slide 158: BREADBOARD 8088 PC #21 MONOCHROME DISPLAY ADAPTOR (MDA#9)

## Slide 159: Monochrome display adapter ACTIVITIES
Update main Address Decoder PLD for IOR/IOW, E, MDARAM & IO A19-A12 all zeros
Update Nanocomp Monitor EEPROM to use IO Ports, set Code and Data Segments
MDA IO Port Decoder PLD, 25 Mhz Dot Clock and Clock PLD
Video RAM, HD68A45S CRTC, IMS G176 Video DAC and 15 Pin VGA Sub D connector
Video Test software to initialize CRTC registers and Video DAC Palette, test basic video output
Character Latch, Character Generator EEPROM and Shift Register, test character output
Add CRT Status register and CRT Control Register and Blink Clock PLD
Add Attribute Latch, Attribute Multiplexer PLD and Video Output PLD
Test MDA Video Controller in ‘Black & White’ Monochrome
Test MDA Video Controller in Colour!

## Slide 160: MDA ATTRIBUTES
Attribute 7 – Blink 0x80-0xFF or Intensity On for Background
Attribute 3 – Intensity On Foreground
Attribute 0-2 = 001 Underline (010, 011,100,101, 110 treated as 111 for foreground, 000 for background)
111 & 000 Normal Video, 000 & 111 Reverse Video, 000 & 000 No Video,
Image from https://www.seasip.info/VintagePC/mda.html

## Slide 161
https://www.aceinnova.com/en/electronics/cga-and-the-brown-color-in-ibm-5153-color-display/

## Slide 162
From int10h.org https://int10h.org/blog/2022/06/ibm-5153-color-true-cga-palette/
  True CGA from CRT Gun voltages
    0xAA – 0xC4 (0x31)
    0x55 – 0x4E (0x13)
    0xDC (0x37)
    0xFF – 0xF3 (0x3C)
    Brown 0xAA5500 – 0xC47E00 (0x31 1F 00)
    0xFFFFFF – 0xFFFFFF (0x3F 3F 3F)

## Slide 163: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
PS/2 Keyboard Controller
Interrupt Controller
Timer
Real time clock
DMA Controller
Floppy Disk Controller
POST Port
BIOS
Boot MS-DOS from Floppy Disk
IDE Disk Controller
IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 164: BREADBOARD 8088 PC #22 WHAT MAKES A MICRO IBM PC COMPATIBLE?

## Slide 165: Breadboard PC - Intel 8088 PC-XT Hybrid
OS
Run an early version of MS-DOS (3.3x) or PC-DOS (2.11)
Video
Monochrome Display Adaptor (MDA) compatible
1981 PC and PC-XT
Clock, CPU and bus control, 8-bit ISA Bus
Direct Memory Access (DMA) controller and Timer
8255 Port and Speaker
PC-AT
Real time clock
Dual Interrupt Controllers (IRQ0-15, PC/XT IRQ0-7) Mouse/Network Card
IBM PS/2
PS/2 Keyboard, Mouse and 8042 Controller,
3.5” 1.44MB Floppy Disk Drive & controller
MCGA Display Adaptor (CGA + 640x480 2 colour, 320x200 256 colour)
Compaq Deskpro 386
IDE Disk and Controller
80 x 25 with 8x16 Character ROM for VGA output

## Slide 166: NanOCOMP ‘8088’ Block DIAGRAM – I/O PORT CHANGES
14.3Mhz
Clock
Microprocessor Intel 8088
Reset & Clock
Address Decoder
Address Bus A0..A19
Data Bus D0..D7
Read Only
Memory (ROM)
Random Access Memory (RAM)
Peripheral Interface Adapter (PIA)
Control Signals (RST, MEMR/MEMW, IOR/IOW NMI, IRQ)
A16, A17,A18,A19
LED 7 Segment Display x 8
Keypad 5 x 5
L
S
CN
G
RST
A
B
C
D
AB
7
8
9
E
M
4
5
6
F
R
1
2
3
0
I
4+8 Decoder
Darlington
Driver
PA0-6
PB0-3
Seg A-G
Digit 0-7
Col 0-6
Row 0-3
RST NMI
Buffers & Latches
Bus
Controller
1-10 Decoder
Memory Map
00000-7FFFF RAM (512K)
IO D000,D100 PIA & UART
B0000-B7FFF MDA RAM (4K)
F8000-FFFFF ROM (32K)
3.6Mhz
Clock
FT232RL
Baud Rate
1,843,200 Hz
÷ 16=115,200
÷ 64=28,800
Serial Port (ACIA/UART)
PC USB
Baud Rate
3,686,400 Hz
÷ 16=230,400
÷ 64=57,600

## Slide 167: BREADBOARD 8088 PC – MDA VIDEO DISPLAY
Blink PLD
25.175Mhz
Shift Register
74ALS166
Main Address Bus
Character Generator ROM
Main Data Bus
Row 0-15 (A0-A3)
Character
Clock 3.146Mhz
Dot Clock
Shift Reg. Latch
Video RAM
Dual Port (4Kb)
Vid. Add.
Character 0-255
(A4-A11)
MA1-MA11
Dot Clock
H Sync, V Sync, Display Enable, Cursor
Clock PLD
ATF22V10
D Type Latch
7ALS574
D Type Latch
7ALS574
Attributes/RGBI
DAC
IMS G176
Attribute
Multiplexer
ATF16V8
VGA
Display Enable
Character raster
bits
MA0
Dot Clk/8
CRTC MC6845
Memory Map
B0000-B0FFF VRAM
Port 3B0 Palette Add Wr
Port 3B1 Palette Colour
Port 3B2 Palette Mark
Port 3B3 Palette Add Rd
Port 3B4 CRTC Index
Port 3B5 CRTC Data
Port 3B8 CRT Control Port
Port 3BA CRT Status Port
H Sync
V Sync
Video Out PLD
ATF22V10
Blink Clocks
Cursor
IO Port Decoder
CRT Control
CRT Status
Fore/Back
Video En, Blink En, B/W
Video En, Blink En, B/W

## Slide 168: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
BIOS
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 169: WHAT MAKES A MICRO IBM PC COMPATIBLE?
Uses Intel 8086 compatible instruction set (we are using 8088)
Provides a BIOS compatible with IBM PC Software Interrupts
I/O Ports and Interrupts same as PC (or BIOS configured for differences)
PC ISA 8-bit or 16-bit expansion bus (System Expansion Bus)
Interrupt Controller (needed for Keyboard & Floppy Disk Controller)
Timer, PPI Port B and Speaker (POST Beep codes)
Direct Memory Access Controller DMA (required for Floppy Disk Controller)
  Tandy 1000, PC Jr did not include DMA, Floppy Disk access more complicated!
PC Compatible Keyboard

## Slide 171
System Board Data Flow XT Tech. ref 1-6
X-Bus for expansion via J8, no DMA, not needed
XA – X-Bus
XD – X-Bus
A[19..0] System bus
D[7..0] System bus
Note that only XIOR, XIOW, XMEMR, XMEMR are used for both buses!
X Ctrl
Buffer
8-15 IRQ

## Slide 172
https://minuszerodegrees.net/5160/misc/5160_motherboard_diagrams.htm

## Slide 173
https://minuszerodegrees.net/5160/misc/5160_motherboard_diagrams.htm

## Slide 174
SYS #1
CPU, Clock, Buffers, Bus Ctrl & Interrupt Ctrl
Only used for /CAS

## Slide 175
SYS #2
Clock & Control Logic
DMA Clock needs 50/50 duty cycle not 33/67, 80ns high time min.

## Slide 176
SYS #3
IO & Address Decoding and RAM Refresh
ROM CS x 2

## Slide 177
SYS #4
DMA Controller & DMA logic
Eliminate XD (use Dn) and XA (use An) means U12 not needed
WRTOMAPPGREG (not S)
DMA Page Register 0x80-0x83
POST also 0x80

## Slide 178
SYS #5
X-Bus Buffers XA, XD, Xcrtl and ROM
AENBRD junction missing
Slot 8 Only

## Slide 179
SYS #6 RAM, Parity, Multiplexers and Buffers

## Slide 180
SYS #7 RAM

## Slide 181
SYS #8
Timer, Speaker & RAM DMA refresh

## Slide 182
SYS #9
PIA, Keyboard and XT configuration

## Slide 183
SYS #10
ISA Bus, Slot 8 & Power

## Slide 184
ACA #1
Async Communications Adapter
Slot 8
Jumper

## Slide 186: HYBRID BREADBOARD PC ISSUES
Slot 8 handling Not Required
X-Bus for XD Data and XA Address not required
POST port 0x80 Conflicts with DMA Page Register for DMA0
  BUT DMA0 page register never used!
PPI Port A 0x60 conflicts with VIA82C42 Keyboard Controller PS/2
PPI Port B 0x61 required, use 74LS646 Octal Bus Transceiver and Register
VIA82C42 A0 address line connect to A2 Keyboard Ports 0x60 & 0x64
Consolidated IO Port and Interrupt mapping
Sergey Kiselev 8088 BIOS https://github.com/skiselev/8088_bios

## Slide 187: Consolidated I/O Port and Interrupt mapping
I/O Port No. | Description | Comments
0x00-0x1F | DMA Controller #1 | 
0x20-0x3F | Interupt Controller #1 | 
0x40-0x43 | Interval Timer #1 | 
0x60-0x63 | PPI Port A, B, C & Control | Only Port B required
0x60, 0x64 | Keyboard Controller | Chip A0 mapped to A2
0x80-0x83 | DMA Page Register | Only 81, 82 & 83 used
0x80 | Power On Self Test (POST) | Same as DMA Page Reg 00.
0xA0-0xBF | Interupt Controller #2 | 
0xC0-0xDF | DMA Controller #2 | Not used in XT only 16bit+
0x1F0-0x1F8 | Fixed Disk Controller | PC-XT used 0x320-0x32F, next phase
0x2F8-0x2FF | Parallel Port #2 | 
0x2F8-0x2FE | Serial Port #2 | 
0x378-0x37F | Parallel Port #1 | 
0x3B0-0x3BF | Monochome Display Adapter MDA | Already implemented
0x3D0-0x3DF | Colour Graphics Adaptor CGA | Next Phase
0x3F0-0x3F7 | Diskette Controller | 
0x3F8-0x3FE | Serial Port #1 | Next Phase
0xD000-0xD003 | PIA Controller Keypad & LED Display | Nanocomp compatible PIA
0xE000-0xE001 | MC6850 Serial Controller | Nanocomp compatible COM port
Interrupt | Description | Comments
NMI | Parity | Not used/Nanocomp Monitor Abort
IRQ0 | Timer | Intel 8253 Programmable Timer
IRQ1 | Keyboard | VIA82C42 Keyboard Controller
IRQ2 | Interrupt C.#2 | Cascade for Interrupt Controller #2
IRQ3 | Serial #2 | 
IRQ4 | Serial #1 | 
IRQ5 | Parallel #2 | PC-XT used this for Fixed Disk
IRQ6 | Diskette C. | 
IRQ7 | Parallel #1 | 
IRQ8 | Real Time Clock | PC-AT Onwards RTC
IRQ9 | Expansion Bus | 
IRQ10 | Expansion Bus | 
IRQ11 | Expansion Bus | 
IRQ12 | Mouse | VIA82C42 Mouse
IRQ13 | Maths Co. Proc. | 8087 Maths Co Processor
IRQ14 | Fixed Disk C. | PC-XT used IRQ5
IRQ15 | Expansion Bus | 

## Slide 188: 8088 BIOS STARTUP SEQUENCE
8255 and PIT Beep Codes
POST Register
DMA Controller (8237)
PIC x 2 (8259)
Initialize PIT (8254 timer)
Initialize PIC (8259)
Keyboard Controller & Mouse
Get video mode (on XT)
Detect Video BIOS and Run
Init Video
Real Time Clock & CMOS
detect_serial
detect_parallel
detect_floppy
detect_ram
test_ram
Detect Extension ROM and run
Boot OS
Check for Setup
Load Boot Sector from Floppy Disk

## Slide 189: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
BIOS
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 190: BREADBOARD 8088 PC #23 PC COMPATIBILITY PART 1 INTERRUPT CONTROLLER, POST, TIMER & PORTB

## Slide 191: WHAT MAKES A MICRO IBM PC COMPATIBLE?
Uses Intel 8086 compatible instruction set (we are using 8088)
Provides a BIOS compatible with IBM PC Software Interrupts
I/O Ports and Interrupts same as PC (or BIOS configured for differences)
PC ISA 8-bit or 16-bit expansion bus (System Expansion Bus)
Interrupt Controller (needed for Keyboard & Floppy Disk Controller)
Timer, PPI Port B and Speaker (POST Beep codes)
Direct Memory Access Controller DMA (required for Floppy Disk Controller)
  Tandy 1000, PC Jr did not include DMA, Floppy Disk access more complicated!
PC Compatible Keyboard

## Slide 192: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
BIOS
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 193
SYS #9
PIA, Keyboard and XT configuration

## Slide 194
SYS #8
Timer, Speaker & RAM DMA refresh
Divide PCLK by 2 for 1.19Mhz

## Slide 195
SYS #1
CPU, Clock, Buffers, Bus Ctrl & Interrupt Ctrl
Only used for /CAS

## Slide 198: WHAT MAKES A MICRO IBM PC COMPATIBLE?
Uses Intel 8086 compatible instruction set (we are using 8088)
Provides a BIOS compatible with IBM PC Software Interrupts
I/O Ports and Interrupts same as PC (or BIOS configured for differences)
PC ISA 8-bit or 16-bit expansion bus (System Expansion Bus)
Interrupt Controller (needed for Keyboard & Floppy Disk Controller)
Timer, PPI Port B and Speaker (POST Beep codes)
Direct Memory Access Controller DMA (required for Floppy Disk Controller)
  Tandy 1000, PC Jr did not include DMA, Floppy Disk access more complicated!
PC Compatible Keyboard

## Slide 199: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
BIOS
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 200: BREADBOARD 8088 PC #24 PC COMPATIBILITY PART 2 BIOS and INSTALL NEW BREADBOARDS

## Slide 202: WHAT MAKES A MICRO IBM PC COMPATIBLE?
Uses Intel 8086 compatible instruction set (we are using 8088)
Provides a BIOS compatible with IBM PC Software Interrupts
I/O Ports and Interrupts same as PC (or BIOS configured for differences)
PC ISA 8-bit or 16-bit expansion bus (System Expansion Bus)
Interrupt Controller (needed for Keyboard & Floppy Disk Controller)
Timer, PPI Port B and Speaker (POST Beep codes)
Direct Memory Access Controller DMA (required for Floppy Disk Controller)
  Tandy 1000, PC Jr did not include DMA, Floppy Disk access more complicated!
PC Compatible Keyboard

## Slide 203: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
BIOS
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 204: STEPS TO GET BIOS RUNNING
Review System Clock and IO Decoder PLD Configs
Install & Test System Clock PLD on CPU/Clock Board
Connect DMA, PIC, PIT, POST and Port B boards to rest of Micro
Test Speaker circuit with 400 Hz test oscillator and monitor POST Port
Download & configure Sergey Kiselev 8088 BIOS https://github.com/skiselev/8088_bios
  Create Breadboard PC configuration & Configure options
  Relocate BIOS Code Segment to RAM 0x68000 (vs ROM 0xF8000)
  Reduce RAM for test to 256Kb (will wipe BIOS from RAM otherwise)
  Change MDA MC6845 register config for VGA 640 x 400 output
  Add VGA DAC Palette config for MDA Video Controller
Load BIOS to 0x6000 code segment via E 6000 Monitor and C 6000 Go FFF0
e_low_ram_test

## Slide 205: BREADBOARD 8088 PC #25 PC COMPATIBILITY PART 3 BIOS and I/O WAIT STATES

## Slide 206: WHAT MAKES A MICRO IBM PC COMPATIBLE?
Uses Intel 8086 compatible instruction set (we are using 8088)
Provides a BIOS compatible with IBM PC Software Interrupts
I/O Ports and Interrupts same as PC (or BIOS configured for differences)
PC ISA 8-bit or 16-bit expansion bus (System Expansion Bus)
Interrupt Controller (needed for Keyboard & Floppy Disk Controller)
Timer, PPI Port B and Speaker (POST Beep codes)
Direct Memory Access Controller DMA (required for Floppy Disk Controller)
  Tandy 1000, PC Jr did not include DMA, Floppy Disk access more complicated!
PC Compatible Keyboard

## Slide 207: WHAT IS A BIOS?
Basic Input/Output System
First BIOS developed by Gary Kildall in 1975 for CP/M
Isolates operating system like CP/M, MS-DOS from hardware differences
Firmware in ROM, EPROM, EEPROM or flash memory
IBM PC-XT BIOS supports 15 Software Interrupt INT BIOS functions
PC BIOS Source Code provided with PC, PC-XT and PC-AT technical reference
Clone PC’s used Phoenix or Award BIOS with Setup Screen
Compaq Portable developed a Clean Room BIOS, Developer never saw IBM BIOS
BIOS provides power on test messages, RAM test and boot failure messages

## Slide 208: STEPS TO GET BIOS RUNNING
Review System Clock and IO Decoder PLD Configs
Install & Test System Clock PLD on CPU/Clock Board
Connect DMA, PIC, PIT, POST and Port B boards to rest of Micro
Test Speaker circuit with 400 Hz test oscillator and monitor POST Port
Download & configure Sergey Kiselev 8088 BIOS https://github.com/skiselev/8088_bios
  Create Breadboard PC configuration & Configure options
  Relocate BIOS Code Segment to RAM 0x68000 (vs ROM 0xF8000)
  Reduce RAM for test to 256Kb (will wipe BIOS from RAM otherwise)
  Change MDA MC6845 register config for VGA 640 x 400 output
  Add VGA DAC Palette config for MDA Video Controller
Load BIOS to 0x6000 code segment via E 6000 Monitor and C 6000 Go FFF0

## Slide 209: POWER ON SELF TEST BEEPS
Tested Speaker Output circuit in last video
MDATest9.asm enables Timer OUT2 at 400Hz
XI 8088 uses 8254 Timer Chip to drive speaker from OUT2 at 400Hz
8254 difficult to buy, I have 8253 instead (ALMOST the same!)
Only signal from speaker is 18.2Hz NOT 400Hz
18.2 Hz is the system timer which uses 65536/0 as the count down timer
  1.19 Mhz / 65536 = 18.2 Hz
Correct divisor sent to Port
BUT /IOW pulse time is 209ns, 8253 Needs 400 ns!

## Slide 210: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
BIOS & I/O Wait States
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 211: BREADBOARD 8088 PC #26 PC COMPATIBILITY PART 4 I/O WAIT STATES AND TEST BIOS

## Slide 212: WHAT MAKES A MICRO IBM PC COMPATIBLE?
Uses Intel 8086 compatible instruction set (we are using 8088)
Provides a BIOS compatible with IBM PC Software Interrupts
I/O Ports and Interrupts same as PC (or BIOS configured for differences)
PC ISA 8-bit or 16-bit expansion bus (System Expansion Bus)
Interrupt Controller (needed for Keyboard & Floppy Disk Controller)
Timer, PPI Port B and Speaker (POST Beep codes)
Direct Memory Access Controller DMA (required for Floppy Disk Controller)
  Tandy 1000, PC Jr did not include DMA, Floppy Disk access more complicated!
PC Compatible Keyboard

## Slide 213: POWER ON SELF TEST BEEPS
Tested Speaker Output circuit in last video
MDATest9.asm enables Timer OUT2 at 400Hz
XI 8088 uses 8254 Timer Chip to drive speaker from OUT2 at 400Hz
8254 difficult to buy, I have 8253 instead (ALMOST the same!)
Only signal from speaker is 18.2Hz NOT 400Hz
18.2 Hz is the system timer which uses 65536/0 as the countdown timer
  1.19 Mhz / 65536 = 18.2 Hz
Correct divisor sent to Port
BUT /IOW pulse time is 210ns, 8253 Needs 400 ns!

## Slide 214
SYS #2
Clock & Control Logic
DMA Clock needs 50/50 duty cycle not 33/67, 80ns high time min.
DMAAEN used by X-Bus Not Required

## Slide 216: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
BIOS & I/O Wait States
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 217: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
BIOS & I/O Wait States
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 218: BREADBOARD 8088 PC #27 PS/2 KEYBOARD & MOUSE CONTROLLER

## Slide 219: High LEVEL PLAN
Reset and Supervisor
Clock
CPU and NOP free run
Bus Controller, Latches & Buffers
EEPROM, RAM & Address Decoder
LED Display & Keypad
Nanocomp C Monitor
Serial Port, SREC Load & Save
Intel Hex file Load & Send
MDA Video Controller
POST Port
Interrupt Controller
Timer & PPI Port B
BIOS & I/O Wait States
PS/2 Keyboard Controller
DMA Controller
Floppy Disk Controller
Boot MS-DOS from Floppy Disk
Real time clock
IDE Disk Controller & IDE BIOS
Boot MS-DOS from Hard Disk
CGA Video Controller
MCGA Enhancement
Serial PPP Networking (dial up)
PS/2 Mouse
Run Windows 1.0/2.0
Network adaptor
Sound Card
Nanocomp ‘8088’
Basic Floppy Disk PC
Disk, Mouse, Windows PC

## Slide 220: PC COMPATIBLE KEYBOARD
Nanocomp 6809 Video #18 includes a lot of background on PC Keyboards
Require “Standard” 102+ Key PC Like Keyboard
  102-106 Keyboard not economic to make and would require PCB
  Modern USB Keyboard needs USB drivers and modern microcontroller
    Prefer 1980’s and early 90’s components, avoiding 21st Century components
  Original PC, PC-XT and PC-AT keyboards difficult to get
  IBM PS/2 compatible 107 Key Keyboard still available £20-25 Amazon
3 Ben Eater Videos on low level PS/2 Keyboard operation
  https://youtu.be/7aXbh9VUB3U
  Covers low level signals, timing and scan codes

## Slide 221: IBM PC KEYBOARDS
PC Generation
PC Model 5150
PC XT Model 5160
PC/AT Model 5170
PS/2 Model 80 (8580)
Keyboard type & interface
83 Key 5 pin DIN (8255 & 74LS322)
83 Key 5 pin DIN (8255 & 74LS322)
84 Key, Enhanced 101/102 Key 5 pin DIN (8042)
Enhanced 101/102 Key with PS/2 6 pin mini DIN (8042)

## Slide 222: #18 NANOCOMP KEYBOARD
Use Standard PS/2 Keyboard with 6 pin mini DIN plug/socket
Intel 8042 microcontroller with keyboard BIOS difficult to find
VIA VT82C42N 40 pin DIP Keyboard Controller £3-5 eBay
  The VT82C42 is a compatible direct replacement for the Intel 80C42 BIOS version of the Keyboard Controller. The VT82C42 is fully implemented by hardware logic so that it has a very fast response capability for any command issued by the host. In addition to keyboard support, the VT82C42 also offers PS/2 mouse support.
  Intel 8042 Used in PS/2 and Compaq Deskpro 386
  Pin Out looking into socket from the front